ONOS Applications

■ org.onosproject.gui2
→ provides ONOS Web GUI;

■ org.onosproject.optical-model
→ provides optical-specific abstractions;
→ Configurable by Network Config Service (onos-netcfg);

■ org.onosproject.openflow-base
→ Provides OpenFlow connection between ONOS and OVS ap/switches;
→ Exposed endpoints:
GET/DELETE http://localhost:8181/onos/v1/devices
GET/POST http://localhost:8181/onos/v1/devices/ports

■ org.onosproject.openflow
→ Installs OpenFlow rules on OVS ap/switches, converts OpenFlow events into ONOS	events, collecting OpenFlow stats (ports, stats, tables);
→ Configurable by Network Config Service (onos-netcfg);
→ Exposed endpoints:
GET/POST/DELETE http://localhost:8181/onos/v1/flows
GET/POST/DELETE http://localhost:8181/onos/v1/groups
GET/POST/DELETE http://localhost:8181/onos/v1/meters
GET http://localhost:8181/onos/v1/statistics/ports
GET http://localhost:8181/onos/v1/statistics/flows

■ org.onosproject.openflow-message
→ Debugging tool to inspect OpenFlow messages;

■ org.onosproject.drivers
→ Provides OpenFlow device drivers;

■ org.onosproject.hostproviders
→ Discovers host devices via ARP or NDP;
→ Configurable by Network Config Service (onos-netcfg);
→ Exposed endpoints:
GET/POST/DELETE http://localhost:8181/onos/v1/hosts

■ org.onosproject.lldpprovider
→ Discovers links between OVS devices via LLDP;
→ Configurable by Network Config Service (onos-netcfg);
→ Exposed endpoints:
GET/POST/DELETE http://localhost:8181/onos/v1/links

■ org.onosproject.linkdiscovery
→ Discovers links between OVS devices via alternative techniques;
→ Configurable by Network Config Service (onos-netcfg);
→ Exposed endpoints:
GET/POST/DELETE http://localhost:8181/onos/v1/links

■ org.onosproject.linkprops
→ Statically configures links properties (bandwidth, latency, cost, etc);
→ Configurable by Network Config Service (onos-netcfg);
→ Exposed endpoints:
GET/POST/DELETE http://localhost:8181/onos/v1/linkprops

■ org.onosproject.metrics
→ Collects metrics about ONOS subsystems (topology, intents, flows, and ports);
→ Exposed endpoints:
GET http://localhost:8181/onos/v1/metrics

■ org.onosproject.nodemetrics
→ Collects metrics about ONOS instance/cluster (CPU, memory, threads);
→ Exposed endpoints:
GET http://localhost:8181/onos/v1/metrics
GET http://localhost:8181/onos/v1/cluster

■ org.onosproject.openstacktelemetry
→ Collects stats about ports, queues, and flows and exports them. Tailored to OpenStack
        deployments;
→ Configurable by Network Config Service (onos-netcfg);
→ Exposed endpoints:
GET http://localhost:8181/onos/openstacktelemetry/ports
GET http://localhost:8181/onos/openstacktelemetry/flows
GET http://localhost:8181/onos/openstacktelemetry/queues

■ org.onosproject.packet-stats
→ Collects stats about control plane traffic;
→ Configurable by Network Config Service (onos-netcfg);
→ Exposed endpoints:
GET http://localhost:8181/onos/packet-stats/packets

■ org.onosproject.yang
→ Runtime YANG ↔ Java translation, exposing YANG-modeled data;
→ Configurable with Karaf command feature:install onos-app-yang
→ Installation folder: ~/onos/apps/yang
→ Exposed endpoints:
GET http://localhost:8181/onos/v1/yang/modules
GET http://localhost:8181/onos/v1/yang/schemas
GET http://localhost:8181/onos/v1/yang/instances

■ org.onosproject.models.ietf
→ Provides predefined IETF standard YANG models;
→ Configurable with Karaf command feature:install onos-app-models-ietf
→ Installation folder: ~/onos/models/ietf
→ Exposed endpoints:
GET http://localhost:8181/onos/v1/yang/ietf-interfaces:interfaces
GET http://localhost:8181/onos/v1/yang/ietf-network:networks

■ org.onosproject.models.openconfig
→ Provides predefined OpenConfig standard YANG models;
→ Configurable with Karaf command feature:install onos-app-models-openconfig
→ Installation folder: ~/onos/models/openconfig
→ Exposed endpoints:
GET http://localhost:8181/onos/v1/yang/openconfig-interfaces:interfaces
GET http://localhost:8181/onos/v1/yang/openconfig-platform:components
GET http://localhost:8181/onos/v1/yang/openconfig-telemetry:telemetry

■ org.onosproject.models.common
→ Provides shared YANG types and structures between IETF and OpenConfig;
→ Configurable with Karaf command feature:install onos-app-models-common
→ Installation folder: ~/onos/models/commons

■ org.onosproject.config
→ Dynamic configuration sub-system;
→ Configurable by Network Config Service (onos-netcfg);
→ Exposed endpoints:
GET/POST/DELETE http://localhost:8181/onos/v1/configurations

■ org.onosproject.netcfghostprovider
→ Statically injects host devices in ONOS;
→ Configurable by Network Config Service (onos-netcfg);

■ org.onosproject.netcfglinksprovider
→ Statically injects links in ONOS;
→ Configurable by Network Config Service (onos-netcfg);

■ org.onosproject.netcfg-monitor
→ Debugs/logs netcfg entries;

■ org.onosproject.reactive-routing
→ Installs flow rules reactively on OVS devices (Aps/switches);
→ Configurable by Network Config Service (onos-netcfg);
→ Exposed endpoints:
GET http://localhost:8181/onos/v1/reactiverouting/routes
GET http://localhost:8181/onos/v1/reactiverouting/nextHops
GET http://localhost:8181/onos/v1/reactiverouting/peers

■ org.onosproject.network-troubleshoot
→ Connectivity diagnostic tool;
→ Exposed endpoints:
GET http://localhost:8181/onos/v1/troubleshoot/connectivity
GET http://localhost:8181/onos/v1/troubleshoot/intents

■ org.onosproject.pathpainter
→ Highlights paths in topology view;
→ Exposed endpoints:
GET/POST/DELETE http://localhost:8181/onos/v1/pathpainter/paths

■ org.onosproject.mobility
→ Handles hosts mobility by tracking their attachment points and modifying flow rules
    accordingly;

ONOS CLI COMMANDS

onos> app [options] [command] [name1 name2 ...]
DESCRIPTION: manages applications inventory
ARGUMENTS:
command: download/install/uninstall/activate/deactivate (required)
        names: application name(s) or URL(s) (required, multi-valued)
OPTIONS:
       --help: display command docs
        -j, --json: output JSON

onos> app-ids [options]
DESCRIPTION: lists ONOS apps IDs
OPTIONS:
        --help: display command docs
        -j, --json: output JSON

onos> apps [options]
DESCRIPTION: lists ONOS apps and their info
OPTIONS:
        --help: display command docs
        -j, --json: output JSON
        -n, --name: sort apps by name
        -s, --short: short output
        -a, --active: show active apps only

onos> cfg [options] [command] [component name] [property name] [property value]
DESCRIPTION: manages JAVA-OSGi components configuration
ARGUMENTS:
command: get/set/preset
component name
property name
property value
OPTIONS:
       --help: display command docs
       -j, --json: output JSON
       -s, --short: short output

onos> netcfg [options] [entity type] [entity ID] [configuration field]
DESCRIPTION: manages network configuration (network-related data modelling)
ARGUMENTS:
entity type
entity ID
configuration field
OPTIONS:
       --help: display command docs
       -j, --json: output JSON
       --remove: remove specified configuration

onos> netcfg-registry [options]
DESCRIPTION: displays registry of network configuration
OPTIONS:
       --help: display command docs
       -j, --json: output JSON
       -s, --short: short output

onos> nodes [options]
DESCRIPTION: lists all controller nodes
OPTIONS:
       --help: display command docs
       -j, --json: output JSON

onos> devices [options]
DESCRIPTION: list all OVS devices (APs/switches)
OPTIONS:
       --help: display command docs
       -j, --json: output JSON
       -s, --short: short output only

onos>device-controllers [options] [OVS device ID] *** (need to enable an app?)
DESCRIPTION: list controller instances for a given OVS device
ARGUMENTS:
OVS device ID (required)
OPTIONS:
       --help: display command docs
       -j, --json: output JSON

onos> device-drivers [options] [OVS device ID]
DESCRIPTION: displays driver for OVS devices
ARGUMENTS:
OVS device ID
OPTIONS:
        --help: display command docs
        -j, --json: output JSON

onos> device-interfaces [options] [OVS device ID]
DESCRIPTION: displays L3 interfaces for OVS devices
ARGUMENTS:
OVS device ID
OPTIONS:
       --help: display command docs
       -j, --json: output JSON
       -s, --short: short output

onos> drivers [options] [driver name]
DESCRIPTION: list all available drivers
ARGUMENTS:
driver name
OPTIONS:
       --help: display command docs
       -j, --json: output JSON
       -s, --short: short output

onos> driver-providers [options]
DESCRIPTION: displays driver providers for OVS devices
OPTIONS:
        --help: display command docs
        -j, --json: output JSON

onos> hosts [options]
DESCRIPTION: lists all currently known host devices
OPTIONS:
        --help: display command docs
        -j, --json: output JSON
        -s, --short: short output

onos> interfaces [options]
DESCRIPTION: displays L3 interfaces
OPTIONS:
        --help: display command docs
       -j, --json: output JSON
        -s, --short: short output

onos> ports [options] [OVS device ID]
DESCRIPTION: displays L2 ports for OVS devices
ARGUMENTS:
OVS device ID
OPTIONS:
        --help: display command docs
        -j, --json: output JSON
        -s, --short: short output
        -e, --enabled: show only enabled pors
        -d, --disabled: show only disabled ports

onos> edge-ports [options] [OVS device ID]
DESCRIPTION: displays L2 edge ports (towards hosts) for OVS devices
ARGUMENTS:
OVS device ID
OPTIONS:
        --help: display command docs
        -j, --json: output JSON

onos> portstate [options] [OVS device ID] [port number] [state]
DESCRIPTION: enable/disable an L2 port on an OVS device
ARGUMENTS:
OVS device ID
port number
state: enable/disable
OPTIONS:
        --help: display command docs
        -j, --json: output JSON

onos> portstats [options] [OVS device ID] [port number]
DESCRIPTION: lists statistics of an L2 port on an OVS device

ARGUMENTS:
OVS device ID
port number
OPTIONS:
        --help: display command docs
        -j, --json: output JSON
       -nz, --nonzero: shows only non-zero stats
       -d, --delta: shows port stats for last polling interval
       -t, --table: shows port stats for last polling interval in table format

onos> links [options] [OVS Device ID]
DESCRIPTION: lists infrastructure links for OVS devices
ARGUMENTS:
OVS device ID
OPTIONS:
       --help: display command docs
        -j, --json: output JSON

onos> check-internal-connectivty [options] [device ID/input port] [device ID/output port]
DESCRIPTION: checks if two ports on the same OVS device can be internally connected
ARGUMENTS:
device ID: OVS device ID
input port: port number
output port: port number
OPTIONS:
        --help: display command docs
        -j, --json: output JSON

onos> config-link [options] [src] [dst]
DESCRIPTION: configure a link between two OVS devices (APs/switches)
ARGUMENTS:
src: device ID + port number (required)
dst: device ID + port number (required)
OPTIONS:
        --help: display command docs
        -j, --json: output JSON
        --type [VALUE]: DIRECT (default)/INDIRECT/TUNNEL/OPTICAL/EDGE
        --disallow: blacklists the link
        --uni-directional: marks the link as uni-directional
        --bandwidth [INT]: set link capacity in Mbps
        --remove-config: remove configuration on this link

onos> config-link-discovery [options] [OVS device ID] [port number]
DESCRIPTION: enable/disable LLDP discovery on a given OVS device
ARGUMENTS:
OVS device ID (required)
port number
OPTIONS:
        --help: display command docs
        -j, --json: output JSON
        -r, --remove: disable LLDP discovery
        --enable: enable LLDP discovery
onos> annotate-device [options] [OVS device ID] [annotation key] [value]
DESCRIPTION: add a transient annotation (extra metadata) on OVS devices
ARGUMENTS:
        OVS device ID (required)
        annotation key (required)
        value (optional, null to remove the transient annotation)
OPTIONS:
        --help: display command docs
        -j, --json: output JSON
        --remove-config: remove persistent annotation

onos> annotate-host [options] [host ID] [annotation key] [value]
DESCRIPTION: add a transient annotation (extra metadata) on host devices
ARGUMENTS:
        host ID (required)
        annotation key (required)
        value (optional, null to remove the transient annotation)
OPTIONS:
        --help: display command docs
        -j, --json: output JSON
        --remove-config: remove persistent annotation

onos> annotate-link [options] [src device/port] [dst device/port] [annotation key] [value]
DESCRIPTION: add a transient annotation (extra metadata) on links between OVS devices
        (APs/switches)
ARGUMENTS:
        device: OVS device ID (required for both source and destination)
port: port number (required for both source and destination)
annotation key (required)
value (optional, null to remove the transient annotation)
OPTIONS:
--help: display command docs
       -j, --json: output JSON
--both: apply annotatation on both directions

onos> annotate-port [options] [device/port] [annotation key] [value]
DESCRIPTION: add a transient annotation (extra metadata) on OVS devices L2 ports
ARGUMENTS:
        device: OVS device ID (required)
port: port number (required)
annotation key
value (optional, null to remove the transient annotation)
OPTIONS:
        --help: display command docs
        -j, --json: output JSON
        --remove-config: remove persistent annotation

onos> paths [options] [src] [dst]
DESCRIPTION: list all shortest path and their cost (default metric: hops count) between two OVS
   devices (APs/switches)
ARGUMENTS:
src: OVS device ID (required)
dst: OVS device ID (required)
OPTIONS:
        --help: display command docs
        -j, --json: output JSON
        -r, --recompute: trigger topology re-computation
        --disjoint: shows disjointed paths only

onos> flows [options] [state] [OVS device ID] [table ID]
DESCRIPTION: list all known OpenFlow rules
ARGUMENTS:
state: PENDING_ADD/ADDED/PENDING_REMOVE/REMOVED
OVS device ID
table ID (integer)
OPTIONS:
        --help: display command docs
        -j, --json: output JSON
        -s, --short: short output
        -c, --count: print flow count
        -n, --no-core-flows: shows only flow rules not installed by ONOS core apps
        -f, --filter [word1 word2 …]: shows only flow rules containing all key-words
        -r, --remove [word1 word2 …]: remove flow rules containing all key-words

onos> get-flow-stats [options] [device ID/port]
DESCRIPTION: list flow stats for a given connection point
ARGUMENTS:
device ID: OVS device ID (required)
port: port number (required)
OPTIONS:
        --help: display command docs
        -j, --json: output JSON
        -s, --summary=[true/false]: shows flow stats summary
        -a, --all: shows all available stats
        -i, --instructionType [TYPE]: DROP/OUTPUT/GROUP/L0MODIFICATION/
        L2MODIFICATION/TABLE/ L3MODIFICATION/METADATA
        -i, --flowType [TYPE]: IMMEDIATE/SHORT/MID/LONG/UNKNOWN

onos> groups [options] [state] [OVS device ID]
DESCRIPTION: list all known OpenFlow group rules
ARGUMENTS:
        state: PENDING_ADD/ADDED/PENDING_REMOVE/REMOVED
OVS device ID
OPTIONS:
--help: display command docs
        -j, --json: output JSON
-c, --count: print group count
        -r, --referenced: print only group rules references in OpenFlow rules
        -u, --unreferenced: print only groupt rules not referenced in OpenFlow rules
        -t, --type [TYPE]: ALL/SELECT/INDIRECT/FAST_FAILOVER

onos> get-stats [options] [device/port]
DESCRIPTION: fetches statistics fro a port of an OVS device (APs/switches)
ARGUMENTS:
device ID: OVS device ID (required)
port: port number (required)
OPTIONS:
--help: display command docs
        -j, --json: output JSON

onos> metrics [options] [metric name]
DESCRIPTION: displays measured metrics
ARGUMENTS:
metric name
OPTIONS:
--help: display command docs
        -j, --json: output JSON

ONOS REST-API Endpoints

http://localhost:8181/onos/v1/docs/#/
comprehensive documentation about exposed ONOS REST-API endpoints

GET http://localhost:8181/onos/v1/applications
returns list of all installed applications
GET http://localhost:8181/onos/v1/applications/ids
returns list of IDs of all installed applications
GET http://localhost:8181/onos/v1/applications/{app name}
get details of a specific application
GET http://localhost:8181/onos/v1/applications/{app name}/bits
get OAR/JAR file of a specific application
POST http://localhost:8181/onos/v1/applications/{app name}/active
activate a specific application
DELETE http://localhost:8181/onos/v1/applications/{app name}/active
deactivate a specific application

GET http://localhost:8181/onos/v1/configuration
lists runtime configuration of JAVA components
GET http://localhost:8181/onos/v1/configuration/{component name}
gets runtime configuration of a specific JAVA component
GET http://localhost:8181/onos/v1/configuration/{component name}/{attribute name}
gets a specific configuration attribute of a specific JAVA componenet
POST http://localhost:8181/onos/v1/configuration/{component name}
modifies runtime configuration attributes of a specific JAVA component
DELETE http://localhost:8181/onos/v1/configuration/{component name}
clears configuration attributes of a specific JAVA component

GET http://localhost:8181/onos/v1/topology
gets overview of current topology
GET http://localhost:8181/onos/v1/topology/clusters
lists all clusters in the current topology (each has a dedicated controller instance)
GET http://localhost:8181/onos/v1/topology/clusters/{cluster id}
gets details of a specific cluster
GET http://localhost:8181/onos/v1/topology/clusters/{cluster id}/devices
lists the IDs of all OVS devices (APs/switches) of a specified cluster
GET http://localhost:8181/onos/v1/topology/clusters/{cluster id}/links
lists all links between OVS devices (no edge links) of a specified cluster
GET http://localhost:8181/onos/v1/topology/infrastructure/{device ID: port number}
specifies wheter a given port is part of an edge link or an internal link
GET http://localhost:8181/onos/v1/topology/broadcast/{device ID: port number}
specifies wheter a given port allows flooding of broadcast packets

GET http://localhost:8181/onos/v1/devices
lists all OVS devices (APs and switches)
GET http://localhost:8181/onos/v1/devices/{device id}
gets info on a specific OVS device
GET http://localhost:8181/onos/v1/devices/ports
lists all L2 ports of OVS devices (APs and switches)
GET http://localhost:8181/onos/v1/devices/{device id}/ports
lists all L2 ports of a specific OVS device
POST http://localhost:8181/onos/v1/devices/{device id}/portstate/{port number}
enable/disable a specific L2 port on a given OVS device

GET http://localhost:8181/onos/v1/hosts
lists all host devices in the topology
GET http://localhost:8181/onos/v1/hosts/{host id}
gets info on a specific host device

GET http://localhost:8181/onos/v1/links
gets info about all links between OVS devices (no edge links) in the topology

GET http://localhost:8181/onos/v1/network/configuration
gets all configurations of network components (OVS devices, ports, hosts, links, apps)
GET http://localhost:8181/onos/v1/network/configuration/{component class}
gets configurations of all network components of a specified class
GET http://localhost:8181/onos/v1/network/configuration/{component class}/{component ID}
gets configurations of a specific network component
GET http://localhost:8181/onos/v1/network/configuration/{component class}/{component ID}/{attribute name}
gets a specific configuration attribute of a specific network component
POST http://localhost:8181/onos/v1/network/configuration
modifies all configurations of network components (OVS devices, ports, hosts, links, apps)
POST http://localhost:8181/onos/v1/network/configuration/{component class}
modifies configurations of all network components of a specified class
POST http://localhost:8181/onos/v1/network/configuration/{component class}/{component ID}
modifies configurations of a specific network component
POST http://localhost:8181/onos/v1/network/configuration/{component class}/{component ID}/{attribute name}
modifies a specific configuration attribute of a specific network component
DELETE http://localhost:8181/onos/v1/network/configuration
clears all configurations of network components (OVS devices, ports, hosts, links, apps)
DELETE http://localhost:8181/onos/v1/network/configuration/{component class}
clears configurations of all network components of a specified class
DELETE http://localhost:8181/onos/v1/network/configuration/{component class}/{component ID}
clears configurations of a specific network component
DELETE http://localhost:8181/onos/v1/network/configuration/{component class}/{component ID}/{attribute name}
clears a specific configuration attribute of a specific network component

GET http://localhost:8181/onos/v1/paths/{src device ID}/{dst device ID}
returns a list of minimum-cost paths between any two devices (both hosts and OVS	devices) in the network. It also includes edge links. Default configuration: Djikstra	algorithm with hop count metric
GET http://localhost:8181/onos/v1/paths/{src device ID}/{dst device ID}/disjoint
same as before, but it returns only paths with no links in common

GET http://localhost:8181/onos/v1/flows
get all known flow rules in the network
GET http://localhost:8181/onos/v1/flows/{device id}
get all flow rules installed in a specific OVS device (AP/switch)
GET http://localhost:8181/onos/v1/flows/{device id}/{flow id}
get a specific flow rule installed in a specific OVS device (AP/switch)
GET http://localhost:8181/onos/v1/flows/{table id}
get all known flow rules in a specific table, across all OVS devices
POST http://localhost:8181/onos/v1/flows
installs a flow rule
POST http://localhost:8181/onos/v1/flows/{device id}
installs a flow rule in a specific OVS device (AP/switch)
DELETE http://localhost:8181/onos/v1/flows
deletes flow rules
DELETE http://localhost:8181/onos/v1/flows/{device id}/{flow id}
deletes a specifc flow rule in a specific OVS device (AP/switch)

GET http://localhost:8181/onos/v1/groups
gets all known group rules
GET http://localhost:8181/onos/v1/groups/{device id}
gets all group rules installed in a specific OVS device (AP/switch)
POST http://localhost:8181/onos/v1/groups/{device id}
installs a group rule in a specific OVS device (AP/switch)

GET http://localhost:8181/onos/v1/meters
gets all known meters
GET http://localhost:8181/onos/v1/meters/{device id}
gets all meters installed in a specific OVS device (AP/switch)
GET http://localhost:8181/onos/v1/meters/{device id}/{meter id}
get a specific meter installed in a specific OVS device (AP/switch)
POST http://localhost:8181/onos/v1/meters/{device id}
install a meter in a specific OVS device (AP/switch)
DELETE http://localhost:8181/onos/v1/meters/{device id}/{meter id}
deletes a specific meter in a specific OVS device (AP/switch)

GET http://localhost:8181/onos/v1/metrics
gets all available system metrics
GET http://localhost:8181/onos/v1/metrics/{metric name}
gets a specific metric

GET http://localhost:8181/onos/v1/statistics/ports
gets statistics about L2 ports of all OVS devices (APs/switches)
GET http://localhost:8181/onos/v1/statistics/ports/{device ID}
gets statistics about L2 ports of a specific OVS device
GET http://localhost:8181/onos/v1/statistics/ports/{device ID}/{port number}
gets statistics about a specific L2 of a specific OVS device
GET http://localhost:8181/onos/v1/statistics/delta/ports
gets last-polling interval statistics about L2 ports of all OVS devices (APs/switches). Default	polling interval duration is 5 s, it can be changed by modifying attribute	portStatsPollFrequency in	configuration org.onosproject.provider.of.device.impl.OpenFlowDeviceProvider:
GET http://localhost:8181/onos/v1/statistics/delta/ports/{device ID}
gets last-polling interval statistics about L2 ports of a specific OVS device
GET http://localhost:8181/onos/v1/statistics/delta/ports/{device ID}/{port number}
gets last-polling interval statistics about a specific L2 of a specific OVS devic
GET http://localhost:8181/onos/v1/statistics/flows/tables
gets flow table statistics of all OVS devices (APs/switches)
GET http://localhost:8181/onos/v1/statistics/flows/tables/{device ID}
gets flow table statistics of a specific OVS device

GET http://localhost:8181/onos/v1/system
returns current status of ONOS controller cluster

GET http://localhost:8181/onos/v1/packets/processors
returns a list of registered packet processor components

ONOS Flow Rules Format

During a flow POST request to the ONOS REST APIs the passed JSON data can contain different objects in the criteria array . This is an example of a JSON document with all the possible criterion. Any combination of zero or more of these criterion will work in a POST request.
{ / "priority": 40000, / "timeout": 0, / "isPermanent": true, / "deviceId": "of:0000000000000001", / "treatment": { / "instructions": [ / { / "type": "OUTPUT", / "port": "CONTROLLER" / } / ] / }, / "selector": { / "criteria": [ / { / "type": "ETH_TYPE", / "ethType": "0x88cc" / }, / { / "type": "ETH_DST", / "mac": "00:00:11:00:00:01" / }, / { / "type": "ETH_SRC", / "mac": "00:00:11:00:00:01" / }, / { / "type": "IN_PORT", / "port": "1" / }, / { / "type": "IN_PHY_PORT", / "port": "1" / }, / { / "type": "METADATA", / "metadata": "0x1000" / }, / { / "type": "VLAN_VID", / "vlanId": "1" / }, / { / "type": "VLAN_PCP", / "priority": "1" / }, / { / "type": "INNER_VLAN_VID", / "innerVlanId": "1" / }, / { / "type": "INNER_VLAN_PCP", / "innerPriority": "1" / }, / { / "type": "IP_DSCP", / "ipDscp": 1 / }, / { / "type": "IP_ECN", / "ipEcn": 1 / }, / { / "type": "IP_PROTO", / "protocol": 1 / }, / { / "type": "IPV4_SRC", / "ip": "10.1.1.0/24" / }, / { / "type": "IPV4_DST", / "ip": "10.1.1.0/24" / }, / { / "type": "TCP_SRC", / "tcpPort": 1 / }, / { / "type": "TCP_DST", / "tcpPort": 1 / }, / { / "type": "UDP_SRC", / "udpPort": 1 / }, / { / "type": "UDP_DST", / "udpPort": 1 / }, / { / "type": "SCTP_SRC", / "sctpPort": 1 / }, / { / "type": "SCTP_DST", / "sctpPort": 1 / }, / { / "type": "ICMPV4_TYPE", / "icmpType": "1" / }, / { / "type": "ICMPV4_CODE", / "icmpCode": 1 / }, / { / "type": "IPV6_SRC", / "ip": "1111::2222/64" / }, / { / "type": "IPV6_DST", / "ip": "1111::2222/64" / }, / { / "type": "IPV6_FLABEL", / "flowlabel": 1 / }, / { / "type": "ICMPV6_TYPE", / "icmpv6Type": 1 / }, / { / "type": "ICMPV6_CODE", / "icmpv6Code": 1 / }, / { / "type": "IPV6_ND_TARGET", / "targetAddress": "1111::2222" / }, / { / "type": "IPV6_ND_SLL", / "mac": "00:00:11:00:00:01" / }, / { / "type": "IPV6_ND_TLL", / "mac": "00:00:11:00:00:01" / }, / { / "type": "MPLS_LABEL", / "label": 1 / }, / { / "type": "IPV6_EXTHDR", / "exthdrFlags": 1 / }, / { / "type": "OCH_SIGID", / "lambda": 1 / }, / { / "type": "GRID_TYPE", / "gridType": DWDM / }, / { / "type": "CHANNEL_SPACING", / "channelSpacing": 100 / }, / { / "type": "SPACING_MULIPLIER", / "spacingMultiplier": 4 / }, / { / "type": "SLOT_GRANULARITY", / "slotGranularity": 8 / }, / { / "type": "OCH_SIGID", / "ochSignalId": 1 / }, / { / "type": "TUNNEL_ID", / "tunnelId": 5 / }, / { / "type": "OCH_SIGTYPE", / "ochSignalType": 1 / }, / { / "type": "ODU_SIGID", / "oduSignalId": 1 / "tributaryPortNumber": 11 / "tributarySlotBitmap": bitmap / "type": "ETH_TYPE", / "tributarySlotLen": 1 / }, / { / "type": "ODU_SIGTYPE", / "oduSignalType": 4 / }, / ] / } / }

## Key and field description
The following table describes the type and the value format of the fields.
KEY	DESCRIPTION	FORMAT
ETH_TYPE	ethernet frame type	int64
ETH_DST	mac address	string
ETH_SRC	mac address	string
IN_PORT	match port	int64
IN_PHY_PORT	match port	int64
METADATA	metadata passed between tables	Hex16
VLAN_VID	vlanId	uint16
VLAN_PCP	Vlan priority	int64
INNER_VLAN_VID	vlanId	uint16
INNER_VLAN_PCP	Vlan priority	int64
IP_DSCP	IP DSCP (6 bits in ToS field)	byte
IP_ECN	IP ECN (2 bits in ToS field).	byte
IP_PROTO	Ip protocol	uint16
IPV4_SRC	source ip	string
IPV4_DST	destination ip	string
TCP_SRC	TCP source address	uint16
TCP_DST	TCP destination address	uint16
UDP_SRC	UDP source address	uint16
UDP_DST	UDP destination address	uint16
SCTP_SRC	SCTP source address	uint16
SCTP_DST	SCTP destination address	uint16
ICMPV4_TYPE	Internet Control Message Protocol for IPV4 type (RFC0792)	uint16
ICMPV4_CODE	Internet Control Message Protocol for IPV4 code (RFC0792)	uint16
IPV6_SRC	source ipv6	string
IPV6_SRC	destination ipv6	string
IPV6_FLABEL	IPv6 Flow Label (RFC 6437)	Hex16
ICMPV6_TYPE	Internet Control Message Protocol for IPV6 type (RFC2463)	uint16
ICMPV6_CODE	Internet Control Message Protocol for IPV6 code (RFC2463)	uint16
IPV6_ND_TARGET	IPv6 Neighbor discovery target address	string
IPV6_ND_SLL	IPv6 Neighbor discovery mac address	string
IPV6_ND_TTL	IPv6 Neighbor discovery ttl mac address	string
MPLS_LABEL	MPLS label	int32
IPV6_EXTHDR	IPv6 extension header pseudo-field	int64
OCH_SIGID	wavelength abstraction	int64
GRID_TYPE	Type of wavelength grid	string
CHANNEL_SPACING	Optical channel spacing	int64
SPACING_MULIPLIER	Optical channel spacing multiplier	int64
OCH_SIGID	Optical channel signal ID	int64
TUNNEL_ID	Tunnel ID	int64
OCH_SIGID	Optical channel signal type	int64
ODU_SIGID	ODU (Optical channel Data Unit) signal ID.	int64
tributaryPortNumber	OPU (Optical channel Payload Unit) port number.	int64
tributarySlotBitmap	OPU (Optical channel Payload Unit) slot length.	int64
tributarySlotLen	OPU (Optical channel Payload Unit) slot bitmap.	array of bytes
ODU_SIGTYPE	ODU (Optical channel Data Unit) signal type.	int64

During a flow POST request to the ONOS REST APIs the passed JSON data can contain different objects in the instructions array . This is an example of a JSON document with all the possible instructions with type and subtype combinations. A combination of one or more of these instructions will work in a POST request.
"treatment": { / "instructions": [ / { / "type": "OUTPUT", / "port": "CONTROLLER" / }, / { / "type": "TABLE", / "tableId": 1 / }, / { / "type": "GROUP", / "groupId": 1 / }, / { / "type": "METER", / "meterId": 1 / }, / { / "type": "QUEUE", / "queueId": 1, / "port": 2 / }, / { / "type": "L0MODIFICATION", / "subtype": "LAMBDA", / "lambda": 1 / }, / { / "type":"L0MODIFICATION", / "subtype":"OCH", / "gridType": "DWDM", / "channelSpacing": 1, / "spacingMultiplier": 1, / "slotGranularity": 1 / }, / { / "type":"L1MODIFICATION", / "subtype":"ODU_SIGID", / "oduSignalId":{ / "tributaryPortNumber": 1, / "tributarySlotLength": 1, / "tributarySlotBitmap": <bitmap> / } / }, / { / "type":"L2MODIFICATION", / "subtype":"VLAN_PUSH" / }, / { / "type":"L2MODIFICATION", / "subtype":"VLAN_ID", / "vlanId":200 / }, / { / "type":"L2MODIFICATION", / "subtype":"VLAN_PCP", / "vlanPcp":0 / }, / { / "type":"L2MODIFICATION", / "subtype":"ETH_SRC", / "mac":"00:00:00:00:01" / } / { / "type":"L2MODIFICATION", / "subtype":"ETH_DST", / "mac":"00:00:00:00:01" / }, / { / "type":"L2MODIFICATION", / "subtype":"MPLS_LABEL", / "label":1 / }, / { / "type":"L2MODIFICATION", / "subtype":"MPLS_PUSH", / "ethernetType":1 / }, / { / "type":"L2MODIFICATION", / "subtype":"TUNNEL_ID", / "tunnelId":1 / }, / { / "type":"L3MODIFICATION", / "subtype":"IPV4_SRC", / "ip":"1.1.1.1" / }, / { / "type":"L3MODIFICATION", / "subtype":"IPV4_DST", / "ip":"1.1.1.1" / }, / { / "type":"L3MODIFICATION", / "subtype":"IPV6_SRC", / "ip":"1111::2222" / }, / { / "type":"L3MODIFICATION", / "subtype":"IPV6_DST", / "ip":"1111::2222" / }, / { / "type":"L3MODIFICATION", / "subtype":"IPV6_FLABEL", / "flowLabel":1 / }, / { / "type":"L4MODIFICATION", / "subtype":"TCP_SRC", / "tcpPort":1 / }, / { / "type":"L4MODIFICATION", / "subtype":"UDP_SRC", / "udpPort":1 / } / ] / }

Subject Class: Host
configKey=basic
subjectKey=org.onosproject.net.HostId configClass=org.onosproject.net.config.basics.BasicHostConfig

configKey=annotations
subjectKey=org.onosproject.net.HostId, configClass=org.onosproject.net.config.basics.HostAnnotationConfig

Subject Class: Devices
configKey=classifiers
subjectKey=org.onosproject.net.DeviceId configClass=org.onosproject.openflow.controller.OpenFlowClassifierConfig

configKey=protection
subjectKey=org.onosproject.net.DeviceId configClass=org.onosproject.net.behaviour.protection.ProtectionConfig

configKey=basic
subjectKey=org.onosproject.net.DeviceId configClass=org.onosproject.net.config.basics.BasicDeviceConfig

configKey=inject
subjectKey=org.onosproject.net.DeviceId configClass=org.onosproject.net.config.inject.DeviceInjectionConfig

configKey=ports
subjectKey=org.onosproject.net.DeviceId configClass=org.onosproject.net.config.basics.PortDescriptionsConfig

configKey=linkDiscovery
subjectKey=org.onosproject.net.DeviceId configClass=org.onosproject.provider.lldp.impl.LinkDiscoveryFromDevice

configKey=openflow
subjectKey=org.onosproject.net.DeviceId configClass=org.onosproject.openflow.config.OpenFlowDeviceConfig

configKey=annotations
subjectKey=org.onosproject.net.DeviceId configClass=org.onosproject.net.config.basics.DeviceAnnotationConfig

Subject Class: Ports
configKey=annotations
subjectKey=org.onosproject.net.ConnectPoint configClass=org.onosproject.net.config.basics.PortAnnotationConfig

configKey=interfaces
subjectKey=org.onosproject.net.ConnectPoint configClass=org.onosproject.net.config.basics.InterfaceConfig

configKey=hostLearning
subjectKey=org.onosproject.net.ConnectPoint, configClass=org.onosproject.net.config.basics.HostLearningConfig

configKey=bandwidthCapacity
subjectKey=org.onosproject.net.ConnectPoint, configClass=org.onosproject.net.config.basics.BandwidthCapacity

configKey=optical
subjectKey=org.onosproject.net.ConnectPoint, configClass=org.onosproject.net.optical.config.OpticalPortConfig

configKey=linkDiscovery
subjectkey=org.onosproject.net.ConnectPoint configClass=org.onosproject.provider.lldp.impl.LinkDiscoveryFromPort

Other Subject Classes
subjectKey=links, configKey=basic, subjectClass=org.onosproject.net.LinkKey, configClass=org.onosproject.net.config.basics.BasicLinkConfig

subjectKey=layouts, configKey=basic, subjectClass=org.onosproject.ui.model.topo.UiTopoLayoutId, configClass=org.onosproject.net.config.basics.BasicUiTopoLayoutConfig

subjectKey=apps, configKey=core, subjectClass=org.onosproject.core.ApplicationId, configClass=org.onosproject.store.link.impl.CoreConfig
subjectKey=apps, configKey=suppression, subjectClass=org.onosproject.core.ApplicationId, configClass=org.onosproject.provider.lldp.impl.SuppressionConfig

subjectKey=regions, configKey=basic, subjectClass=org.onosproject.net.region.RegionId, configClass=org.onosproject.net.config.basics.BasicRegionConfig

{
  "ports": {
    "of:0000000000000021/1": {
      "annotations": {
        "entries": {
        "name": "sw021-eth1",
        "maxQueueLength": "1000",
        "backlogPackets": "45",
        "backlogBytes": "12568",
        "bandwidth": "1000",
        "maxQueueLength": "1000",
        "txPackets": "1876",
        "rxPackets": "3456",
        "txErrors": "78",
        "rxErrors": "36"
        }
      }
    }
  }
}

{
  "ports": {
    "of:0000000000000011/1": {
      "annotations": {
        "entries": {
        "name": "ap011-wlan1",
        "maxQueueLength": "10240",
        "backlogPackets": "45",
        "backlogBytes": "12568",
        "bandwidth": "54",
        "maxQueueLength": "1000",
        "txPackets": "1876",
        "rxPackets": "3456",
        "txErrors": "78",
        "rxErrors": "36",
        "WiFi Mode": "a",
        "Frequency": "5.18",
        "Channel": "36",
        "SSID": "ssid-ap011",
        "txPower": "14",
        "txGain": "10",
        "position": "3.8, 4.0, 8.9",
        "range": "3665"
        }
      }
    }
  }
}

{
  "hosts": {
    "00:00:00:03:02:02/None": {
      "annotations": {
        "entries": {
        "name": "h322",
        "type": "Host",
        "ports": ["1:h322-eth1"]
        }
      }
    }
  }
}

{
  "hosts": {
    "00:00:00:03:00:03/None": {
      "annotations": {
        "entries": {
        "name": "sta303",
        "type": "Station",
        "ports": ["0:sta003-wlan0"],
        "position": "[4.0, 6.4, 8.4]",
        "WiFi Mode": "a",
        "Frequency": "5.18",
        "connectedTo": "ssid-ap301",
        "RSSI": "-67",
        "distanceFromAp": "842.35"
        }
      }
    }
  }
}

{
  "devices": {
    "of:0000000000000301/1": {
      "annotations": {
        "entries": {
        "position": ["692.8, 600.0, 302.89"]
        }
      }
    }
  }
}